Site name: Johson Mesa

Device codes: JE; JG;

Coordinates: S63°49'20.4"; W57°55'57.1"

Altitude: 340 m a. s. l.

Site description: The study site is situated on the top of Johson Mesa in the northwestern part of Ulu Peninsula, James Ross Island. The site provides both atmospheric and ground data. Its surrounding is mostly flat with no geomorphological features to shadow it and it is covered by regolith.

Measured parameters:

Current setting:

F1	- Soil temperature (5 cm) - since 25 January 2013

F2	- Soil temperature (5 cm) - since 25 January 2013

JE	- all measurements since 31 December 2005

- Air temperature and Relative humidity (200 cm)

- Global and Reflected radiation (210 cm from 24 January 2008)

- Surface temperature (1 cm)

- Heat flux 1 (2 cm, 5 cm since 9 January 2015)

- Heat flux 2 (2 cm, 20 cm since 9 January 2015)

- Wind speed and Wind direction (10 m, 5.8 m from 4 February 2007)

- Soil temperature (5, 10, 20 cm)

JG 	- Soil temperature (5, 10, 20, 30, 50, 75 cm) - since 17 February 2011

- Soil moisture (5, 20, 30 cm) - since 12 February 2012

JS	- Snow depth (91 cm) - since 4 February 2012

33	- Soil temperature (15, 30 cm) – since 1 February 2009

94	- Soil temperature (30, 50 cm) – since 14 February 2010

Cancelled measurement:

H2 - Soil moisture (5, 20 cm) - between 14 February 2010 and 12 February 2015

32 - Soil temperature (15, 30 cm) – between 1 February 2009 and 9 January 2015

Measurement interval:

F1 - 60 min

F2 - 60 min

JE - 30 min

JG - 30 min

JS - 180 min

33 - 60 min

94 - 60 min

Total data availability:  JE - cca 88 %, JG – 95%, the rest - not determined yet

Data quality:

JE - there might be some inhomogenities in wind, radiation, soil surface and soil temperature data

JG – data missing in January 2012

JS - occasional apparent mistakes in measurement

H2 – data ends from 20 March 2014; data from 20 cm not reliable

Missing data period:

2006 (JE)

18 February 2011 - 7 March 2011 (13 days JE)

11 February 2013 - 22 February 2013 (11 days JE)

Published data period:

Data files:

Complete time series –

JE_2010_01_12.dcv

JE_2010_01_24.dcv

JE_2010_02_20.dcv

JE_2011_01_14.dcv

JE_2011_02_04.dcv

JE_2011_02_18.dcv

JE_2012_02_04.dcv

JE_2012_03_03.dcv

JE_2013_01_15.dcv

JE_2013_02_11.dcv

JE_2014_01_22.dcv

JE_2014_02_17.dcv

JE_2015_01_09.dcv

JE_2015_01_14.dcv

JE_2015_02_03.dcv

JE_2015_02_12.dcv

JE_2016_01_14.dcv

JE_2016_02_07.dcv

JG_2011_2014.dcv

JG_2014_01_21.dcv

JG_2015_01_09.dcv

JG_2015_02_03.dcv

JG_2015_02_12.dcv

JG_2016_01_14.dcv

JG_2016_02_07.dcv