Site name: Glacier Whisky

Device codes: JV; JW; JY; W1

Coordinates: S63°55'59.6"; W57°56'54.3" (JV; JY); S63°55'48.1"; W57°56'46.0" (JW); S63°55'7.6";  W57°56'30.3" (W1)

Altitude: 356 m a. s. l. (JV; JY), 326 m a. s. l. (JW), 226 m a. s. l. (W1)

Site description: The study site is situated on the Whisky Glacier in the southern part of Ulu Peninsula, James Ross Island. The site provides atmospheric data and it terrain around it is descending to the northeast.

Measured parameters:

Current setting:

JV - Snow depth (changeable) - since 26 January 2016 (station renewed)

JW - Global radiation (changeable), Air temperature and Relative humidity (200 cm), Wind speed and Wind direction (approx. 260 cm) - since 26 January 2016 (station renewed)

JY - Air temperature and Relative humidity (170 cm) – since 17 February 2010

W1 - Air temperature and Relative humidity (200 cm) – since 15 January 2015

Cancelled measurement:

JQ - Global and Reflected radiation (changeable) - between summer 2011 and  summer 2013 JW - Reflected radiation (90 cm) , Air temperature and Relative humidity (160 cm) -  between 20 February 2009 and 2014

JV - Snow depth (changeable) -  between 20 February 2009 and 2014

Measurement interval:

JV – 240 min

JW – 30 min

JY – 60 min

W1 – 60 min

Total data availability: W1, JY - 100 %, JV, JW - not known so far

Data quality: W1, JY: 1 (no missing values so far), JV, JW - not known so far

Missing data period:

Published data period:

Data files:

Complete time series – raw data:

# Comments

Za předpokladu, že v r. 2015 taky staženo bezproblémově - Filip?